Used to hang the mufflers.  A & F-Body utilize 2 Swivel Hangers while G-Body utilize an assembly made up of an “L” shaped bracket with a rubber hanger attached.  Depending on the vehicle, holes may need to be drilled in crosmember above rear of mufflers for A-Body vehicles and F-Body vehicles will require drilling holes in the body above the rear of the mufflers.  (G-body vehicles will attach the “L” bracket part of the assembly to the crossmember above the muffler.

NOTE:  While we have made every effort to design this Headpipe to fit most Header applications.  We know that from time to time situations will arise which will not be accounted for.  To help minimize inconvenience to you, we recommend that you do some measuring, etc., before “tearing off” the old system.  This way, if you have one of the exceptions, you will not have “down time” if your vehicle is a daily driver.  This will enable you to obtain the necessary parts to complete the installation.

NOTE:  The main problem, which sometimes arises, is that of Headers being aimed other than straight back.  In the instructions, we show you how to determine IF this is the case and offer some suggestions on how to handle this.

Muffler length is generally limited to a maximum of 20” case length on A-Body installations and 17” on F & G-Body installations; however, 1st Generation F-Bodies (’67-69) have less room and usually shorter 16” or less mufflers will work better.

Both Walker and Flowmaster mufflers work equally well; however, the mufflers used need to be offset entrance and offset exit on opposite sides.

NOTE:  It is strongly suggested that you check for any missing items with the above list and against the Invoice which should list all items also.  If you will be taking your vehicle someplace to have the system installed, be sure to tell them to read the instructions first.  BEFORE tearing off your old system, look over things such as misaligned headers, headers that are ‘up’ too high so that when collector reducers are mounted, they or any straight extension off them, will interfere or hit the tranny crossmember or anything else that you think might be a problem during installation.  We know that from time to time situations will arise which will not normally be accounted for.

INSTALLATION:

- First, be sure to read through the Thank You and Caution Flyer accompanying these instructions.

- Secondly, read these instructions first, throughout to get a good overview.

- Thirdly, remember, safety first.  Be sure vehicle is secure and remember that pipes can cut (fingers & hands).

- Now, compare hardware with the list above to be sure you have everything before beginning.  NOTE:  To help prevent rust on hardware, you may want to paint all exposed metal before installing.

- Begin by mounting Collector Reducers on end of Headers.  You may want to note now if your headers seem to be pointing straight back.  IF one or both aren’t, they will present problems when it comes time to install the Head Pipes later.  IF you’re not sure, then you can mount the Headpipes onto the reducers and see how they do.

  - If a Headpipe wants to cross over into the driveshaft, then this is telling you the header is pointing inward.

  - If the Headpipe wants to point outward away from the center of the vehicle as it goes back toward the muffler, then this is telling you the header is pointing outward.

The header could be pointing downward or upward.  The Head Pipes are designed so as to allow you to compensate for some error, but if it’s much, then you will be faced with adapting.  Our “No-Weld” Collector Reducers can often help.  Sometimes it will take more than this.  If you’re not sure, give our Tech Dept. a call.  We can offer suggestions if you can tell us exactly what is happening.  See note at end of Instructions.

- Now lets begin with the Collector Reducers.  Mount them now, then mount the Headpipes onto them.  If the Headpipes are positioning correctly, then mount the mufflers onto the ends (G-Body installations – see next item).  Now you probably will have an idea as to if any trimming will be necessary.  If not sure yet, go ahead and determine location of the Muffler Hangers and install them.  This will help you decide exactly where the end of the muffler will be which in turn will help you decide if and how much to trim the Headpipe.

- G-Body Installation:  Same as above except IF you opted to use the 10 Degree Adapters before the muffler, you will need to naturally install them.

- Wen cutting Headpipes to length, always cut “long” as this places the muffler farther rearward.  Remember, you can always shorten the Headpipe, but is hard to add length – unless you have a Tubing Stretcher!

- You may trim off the end of the Collector Reducer also.  Remember, measure and re-measure as it’s easier to trim a little more than to add.  If the Head Pipe doesn’t reach far enough back, then you will need to do one of two things.  Add an extension between the end of the Headpipe and the muffler (we have the extensions) or for a cleaner installation, we have the HL series Head Pipes that are 10” longer than the standard length.  HL Head Pipes are rarely needed and then mostly on the longer wheel base vehicles such as the El Camino and Caballero.  The GTO’s have a tendency to come up short more so than other A-Body vehicles probably because the headers may tend to be shorter.

- Fine-tune the fit.  Once you have trimmed the Head Pipes for proper fit, then begin “fine tuning” the overall fit.  Do not tighten clamps until you have everything fitting.

- Check for leaks upon completion.  Normally good sealing occurs with clamp type installations.  However, ocassionally we run into a situaion where proper sealing is difficult to obtain.  If this is the case, first try rotating the clamp slighly and re-tightening the clamps.  Caution:  too much tightening can crimp the tubing or possibly cause the U-Bolt to “break”.  OR, try relocating the clamp forward or backward from its present position and re-tightening.  Another possibility is to use “muffler cement” which can be purchased from any muffler shop or auto parts outlet.  If there is excessive clearance between the two pipes, or muffler and pipe, then it may be necessary to cut one or more slots in the outer pipe to allow it to compress further for better sealing.  Try to rotate clamps so the bolt part is not pointing downward for a cleaner looking installation.

- Now, it’s time to consider mounting the Balance Tube Kit  (This may be a project for a professional if you don’t have welding equipment handy or the welding skills of a buddy with such).  Both kits are installed the same way.  It is the only part of our system which needs to be welded and luckily this is done last after everything else is in place.  Ideally, to determine the best mounting location, you will need to spray a line of paint on the side of the head pipes from the collector reducer back approximately 20” or so.  With the vehicle running, you can determine at what point the paint stops burning off.  This is where you  want to mount the Balance Tube.  If for some reason there is an obstruction prohibiting this, then mount it as close as possible to that point.  We have found that usually mounting it anywhere 8” – 16” from the collector flange works fine.

- Now that you have determined where to mount it, you need to determine the length.  Remember to allow for the curvature of the Headpipes as you will want to have some curvature on each end of the Balance Tube.  (With Kit B, first install the short piece of pipe into the longer piece and maybe hold together with the Band Clamp – now you know the overall length and determine everything just as if were Kit A).  Remember, better to cut too long than too short.

- Now cut the holes in the side of the Headpipes.  They DO NOT necessarily have to be as big a diameter as the size of the Blanace Tube.  Do not allow parts of the Balance Tube to protrude into the Heapipe as this will impede flow.  IF the hole is cut a little too big OR if the Balance Tube is cut a little short, you can “Fill Weld” in the gaps to make fit.  It will be a good idea to paint the welds with some Hi-Temp aluminized paint as this will help protect it from rust.

Stainless Steel Band Clamp Upgrade Installation:

If you are using Band Clamps, you will need to “flatten out” the little lip that is always on the end of any hanger.  This allows you to slip the end of the hanger into or between the bars of the Band Clamp as pictured here.  The following photos show how to handle attaching most any hanger or bracket to a Band Type Clamp.

See our Web Site:   www.torquetechexh.com          Email:  torque@surfsouth.com

# Text boxes

# GM Headpipe Kit Instructions

Header Applications

Included with this kit are the following:

Either 3½” x 3”, 3½” x 2½”, 3” x 3”, 3” x 2½”, or 2½” x 2½”.

(Comes with all Nuts, Bolts, Washers & Gaskes)

1 piece of straight tubing 22” long.  If you substituted Kit b, then it consists of 1 piece 16” long (expanded on one end), 1 piece 8” long and 1 SS Band Clamp.

Pipes that comes from mufflers forward to collector reducers.  (43” Long)

4 for the head pipes & Mufflers (8 Clamps for G-Body applications where mounting the mufflers at an angle)

Notice on these two photos how the balance tube was installed.

- Collector Reducers

- Balance Tube Kit A

- Head Pipes

- Clamps

2  Muffler Hanger Assemblies

HEADER ANGLED WRONG?

If the collector of one or both headers aim outward, upward or downward (they’re supposed to be straight back and parallel to the ground and fame rails), then we have special collector reducers that may help (we call them ‘no-welds” simply because we have not welded the tubing part of the reducer to the flange).  They are the same as our regular long tapered units otherwise, just not welded – you do that.  These will usually help unless you have a really bad situation.  Installation of these “no-weld” units is relatively simple.

- Mount the flange to the header.

- Insert the tube part of the reducer onto the head pipe and into the hole of the flange.  It will be going into this hole at an angle because of your problem header.

- Tack weld in several places, then take the assembly off  the vehicle and run a bead all the way around.  Check to be sure there is no metal protruding through the flange into the collector area as it will impede or hinder flow.  Grind off if necessary.